## Slide 1
2025 Q4 Net check UK
NSA CDR analysis Belfast, Bristol, Cardiff, Edinburgh, London, Leeds and Sheffield
Notes: Angelo

## Slide 2: Executive Summary
Operator | Main Finding | Recommendation | Potential Scoring Impact
VFE | Higher data failure ratio in all data test, but specially in FDFS DL&UL in Q4 compared to Q3. | E2E analysis | Data services Success Ratio ('Most reliable’) (FDFS DL&UL, Browsing and Video)
 | Improvement in CST in Q4 compared to Q3 and Q2 |  | CALL SETUP TIME (‘Best Network’)
 | Improvement in FDTT DL throughput performance in Q4 vs Q3 (* due to change in the CORE), matching similar trends as in Q2 |  | FDTT DL Throughput
 | Degradation in FDFS DL throughput performance in Q4 vs Q3 (* due to change in the CORE), matching similar trends as in Q2 |  | FDFS DL Transfer Time
 | Higher Interactivity RTT in Q4 compared to Q3, similar figures as in Q2 (*). London showing poorer performance in Q4 compared to Q2. | E2E analysis | Interactivity RTT (‘Best Network’)
 | Throughput performance when connecting to 3UK MOCN nodes mimics the 3UK performance |  | FDTT and FDFS DL&UL Throughput
 | Better Throughput performance when connecting to VFUK MOCN nodes. This relates with the higher NR TDD utilization |  | FDTT and FDFS DL&UL Throughput
Three | High unqualified data sessions in FDFS DL HTTPS test (not RF related) still present in Q4 in NSA CDR. In SA CDR this problem is not present. | E2E analysis. E2E core tracing needed | FDFS DL Success Ratio ('Most reliable')
 | Lower Call Success ratio in Q4 in London compared to Q3 (higher number of VoLTE failures) | Detail Log analysis of failures cases | Call Success Ratio ('Most reliable')
 | Degradation observed in POLQA AVG MOS in Q4 compared to Q3 mainly in Belfast and Sheffield |  | POLQA Avg MOS
 | Throughput performance when connecting to VFUK MOCN nodes mimics the VFUK performance |  | FDTT and FDFS DL&UL Throughput
 | Better Throughput performance when connecting to 3UK MOCN nodes. This relates with the higher NR TDD utilization |  | FDTT and FDFS DL&UL Throughput
(*) In 2025 Q4 Vodafone core is CISCO CORE (as in 2025 Q2) and in 2025 Q3 it was COSMOS ERICSSON

## Slide 3: Netcheck Q4 scoring “Best network”. Drive city
Cities considered: Belfast, Bristol, Cardiff, Edinburgh, London, Leeds and Sheffield.
The ranking points are scaled to a maximum of 1.000 points, providing comparability with the overall Ranking

## Slide 4: Score breakdown
NETCHECK KPIS |  | Score weight (%) | Max score over 1000 | Vodafone | O2 | Three | EE | GAP Vodafone vs EE | GAP Three vs EE
CLASSIC CALLS | CALL SUCCESS RATIO [%] | 14.28% | 142.80 | 137.41 | 133.33 | 124.56 | 132.00 | -5.41 | 7.44
 | CALL SETUP TIME [s] | 1.68% | 16.80 | 15.68 | 16.80 | 16.32 | 16.73 | 1.04 | 0.40
 | CALL SETUP TIME > 15 s [%] | 0.84% | 8.40 | 7.87 | 8.40 | 8.00 | 8.40 | 0.53 | 0.40
 | POLQA < 1.6 [%] | 4.20% | 42.00 | 33.13 | 32.31 | 32.05 | 34.17 | 1.04 | 2.12
 | POLQA [MOS | 1.40% | 14.00 | 13.81 | 13.80 | 13.71 | 13.95 | 0.14 | 0.24
 | DISTURBED & IMPAIRED CALL [%] | 2.80% | 28.00 | 25.89 | 22.02 | 21.91 | 25.88 | 0.00 | 3.98
WHATSAPP CALLS | CALL SUCCESS RATIO [%] | 5.60% | 56.00 | 53.08 | 53.05 | 50.13 | 56.00 | 2.92 | 5.87
 | POLQA < 1.6 [%] | 1.40% | 14.00 | 11.06 | 10.61 | 10.45 | 12.13 | 1.06 | 1.67
 | POLQA [MOS] | 0.47% | 4.70 | 4.11 | 4.10 | 4.10 | 4.15 | 0.04 | 0.04
 | DISTURBED & IMPAIRED CALL [%] | 0.93% | 9.30 | 7.42 | 6.87 | 7.01 | 7.42 | 0.00 | 0.41
Multi RAB | MULTI RAB DATA TRANSFER SUCCESS RATIO [%] | 1.40% | 14.00 | 13.27 | 14.00 | 13.63 | 13.82 | 0.55 | 0.19
TRANSFER | FDFS DL SUCCESS RATIO [%] | 4.68% | 46.80 | 36.37 | 43.65 | 0.00 | 45.16 | 8.79 | 45.16
 | FDFS DL TRANSFER TIME [s] | 3.12% | 31.20 | 28.77 | 29.19 | 27.70 | 31.20 | 2.43 | 3.50
 | FDFS UL SUCCESS RATIO [%] | 2.34% | 23.40 | 15.42 | 18.43 | 19.23 | 19.89 | 4.47 | 0.66
 | FDFS UL TRANSFER TIME [s] | 1.56% | 15.60 | 13.30 | 9.96 | 13.15 | 14.36 | 1.06 | 1.21
 | FDTT DL THROUGHPUT > 2Mbit/s [%] | 3.12% | 31.20 | 28.17 | 29.45 | 16.64 | 29.21 | 1.04 | 12.57
 | FDTT DL THROUGHPUT > 5Mbit/s [%] | 3.90% | 39.00 | 36.35 | 36.37 | 24.77 | 37.16 | 0.82 | 12.39
 | FDTT DL THROUGHPUT > 20Mbit/s [%] | 3.90% | 39.00 | 31.52 | 32.22 | 28.54 | 35.38 | 3.87 | 6.84
 | FDTT DL THROUGHPUT > 100Mbit/s [%] | 2.34% | 23.40 | 20.32 | 19.50 | 19.21 | 21.40 | 1.08 | 2.19
 | FDTT DL THROUGHPUT P90 [Mbit/s] | 2.34% | 23.40 | 21.33 | 18.05 | 23.40 | 23.18 | 1.86 | -0.22
 | FDTT UL THROUGHPUT > 1Mbit/s [%] | 1.56% | 15.60 | 14.94 | 12.89 | 13.44 | 15.36 | 0.42 | 1.93
 | FDTT UL THROUGHPUT > 3Mbit/s [%] | 1.95% | 19.50 | 17.62 | 16.00 | 16.57 | 18.64 | 1.03 | 2.08
 | FDTT UL THROUGHPUT > 10Mbit/s [%] | 1.95% | 19.50 | 15.13 | 13.96 | 14.21 | 16.78 | 1.65 | 2.57
 | FDTT UL THROUGHPUT > 20Mbit/s [%] | 1.17% | 11.70 | 10.29 | 9.73 | 10.12 | 10.73 | 0.44 | 0.61
 | FDTT UL THROUGHPUT P90 [Mbit/s] | 1.17% | 11.70 | 10.30 | 9.83 | 11.70 | 10.22 | -0.09 | -1.48
HTTP/HTTPs BROWSING | BROWSING TIME TO 1MB [ms] | 5.20% | 52.00 | 52.00 | 52.00 | 52.00 | 52.00 | 0.00 | 0.00
 | BROWSING SUCCESS RATIO [%] | 7.80% | 78.00 | 68.55 | 75.12 | 68.87 | 75.53 | 6.98 | 6.66
VIDEO STREAM | VIDEO STREAMING SUCCESS RATIO [%] | 8.32% | 83.20 | 77.20 | 81.92 | 76.73 | 81.14 | 3.94 | 4.41
 | VIDEO STREAMING TTFP >= 10 s [%] | 0.52% | 5.20 | 4.96 | 4.48 | 3.79 | 5.12 | 0.16 | 1.33
 | VIDEO STREAMING IRRITATING EXPERIENCE [%] | 4.16% | 41.60 | 41.34 | 40.96 | 40.30 | 41.48 | 0.13 | 1.18
INTERACTIVITY | INTERACTIVITY PACKET ERROR RATIO [%] | 0.78% | 7.80 | 6.70 | 6.59 | 0.00 | 7.43 | 0.73 | 7.43
 | INTERACTIVITY MEDIAN RTT [MS] | 3.12% | 31.20 | 26.92 | 27.64 | 29.42 | 29.56 | 2.64 | 0.13

## Slide 5: KPIs prioritization: gap Vodafone vs EE
 | Netcheck KPIs | GAP Vodafone vs EE | Type of KPI
TRANSFER | FDFS DL SUCCESS RATIO [%] | 8.79 | Reliable
HTTP/HTTPs BROWSING | BROWSING SUCCESS RATIO [%] | 6.98 | Reliable
TRANSFER | FDFS UL SUCCESS RATIO [%] | 4.47 | Reliable
VIDEO STREAM | VIDEO STREAMING SUCCESS RATIO [%] | 3.94 | Reliable
TRANSFER | FDTT DL THROUGHPUT > 20Mbit/s [%] | 3.87 | Diff
WHATSAPP CALLS | CALL SUCCESS RATIO [%] | 2.92 | Reliable
INTERACTIVITY | INTERACTIVITY MEDIAN RTT [MS] | 2.64 | Diff
TRANSFER | FDFS DL TRANSFER TIME [s] | 2.43 | Diff
TRANSFER | FDTT DL THROUGHPUT P90 [Mbit/s] | 1.86 | Diff
TRANSFER | FDTT UL THROUGHPUT > 10Mbit/s [%] | 1.65 | Diff
TRANSFER | FDTT DL THROUGHPUT > 100Mbit/s [%] | 1.08 | Diff
WHATSAPP CALLS | POLQA < 1.6 [%] | 1.06 | Reliable
TRANSFER | FDFS UL TRANSFER TIME [s] | 1.06 | Diff
CLASSIC CALLS | CALL SETUP TIME [s] | 1.04 | Diff
TRANSFER | FDTT DL THROUGHPUT > 2Mbit/s [%] | 1.04 | Reliable
CLASSIC CALLS | POLQA < 1.6 [%] | 1.04 | Reliable
TRANSFER | FDTT UL THROUGHPUT > 3Mbit/s [%] | 1.03 | Diff
TRANSFER | FDTT DL THROUGHPUT > 5Mbit/s [%] | 0.82 | Diff
Vodafone having highest gap with EE in data success ratio in Q4, all part of reliability definition (almost 25 points gap with EE).
Low-rate DL sessions
Voice qualifiers
Focus Areas Vodafone:
Data Qualifiers
POLQA
Interactivity RTT
Priority
Low-rate UL sessions
Cities considered: Belfast, Bristol, Cardiff, Edinburgh, London, Leeds and Sheffield.

## Slide 6: KPIs prioritization: gap Three vs EE
Cities considered: Belfast, Bristol, Cardiff, Edinburgh, London, Leeds and Sheffield.
 | NETCHECK KPIS | GAP Three vs EE | Type of KPI
TRANSFER | FDFS DL SUCCESS RATIO [%] | 45.16 | Reliable
TRANSFER | FDTT DL THROUGHPUT > 2Mbit/s [%] | 12.57 | Reliable
TRANSFER | FDTT DL THROUGHPUT > 5Mbit/s [%] | 12.39 | Diff
CLASSIC CALLS | CALL SUCCESS RATIO [%] | 7.44 | Reliable
INTERACTIVITY | INTERACTIVITY PACKET ERROR RATIO [%] | 7.43 | Diff
TRANSFER | FDTT DL THROUGHPUT > 20Mbit/s [%] | 6.84 | Diff
HTTP/HTTPs BROWSING | BROWSING SUCCESS RATIO [%] | 6.66 | Reliable
WHATSAPP CALLS | CALL SUCCESS RATIO [%] | 5.87 | Reliable
VIDEO STREAM | VIDEO STREAMING SUCCESS RATIO [%] | 4.41 | Reliable
CLASSIC CALLS | DISTURBED & IMPAIRED CALL [%] | 3.98 | Diff
TRANSFER | FDFS DL TRANSFER TIME [s] | 3.50 | Diff
TRANSFER | FDTT UL THROUGHPUT > 10Mbit/s [%] | 2.57 | Diff
TRANSFER | FDTT DL THROUGHPUT > 100Mbit/s [%] | 2.19 | Diff
CLASSIC CALLS | POLQA < 1.6 [%] | 2.12 | Reliable
TRANSFER | FDTT UL THROUGHPUT > 3Mbit/s [%] | 2.08 | Diff
TRANSFER | FDTT UL THROUGHPUT > 1Mbit/s [%] | 1.93 | Reliable
WHATSAPP CALLS | POLQA < 1.6 [%] | 1.67 | Reliable
Three with highest gap in data qualifier (FDFS DL 45 points gap with EE, browsing and YouTube 11 points).
Low DL throughput samples for FDTT DL showing a gap of 30 points with EE
Voice qualifiers showing 13 points gap.
Low-rate DL sessions
Voice Qualifiers
Focus Areas Three:
Data qualifiers
Disturbed and impaired
Interactivity
POLQA<1.6
Priority

## Slide 7: 7 cities analysis Belfast, Bristol, Cardiff, Edinburgh, London, Leeds and Sheffield

## Slide 8: Completed Call Ratio
Three having worse performance in VoLTE and WhatsApp in Q4.
Small degradation in WhatsApp for Vodafone in Q4.

## Slide 9: Voice failures per Q/city
Three: higher number of Volte and WhatsApp failed calls in London in Q4 compared to Q3.
Vodafone showing similar number of voice failures in Q4 and even improvement in Sheffield figures for VoLTE service.

## Slide 10: Data failure
Worse data qualifiers in Q4 for Vodafone compared to Q3 for all data services.
Biggest gap on FDFS DL&UL

## Slide 11: Data failures - FDFS test
Three: failures in Q4 in FDFS coming from https DL as already known
Vodafone: increased of data failures in FDFS DL&UL in Q4. Higher FDFS UL failure ratio compared to three and EE in Q4.

## Slide 12: POLQA AVG MOS (Multirab&volte)
Degradation observed in Three in POLQA AVG MOS in Q4 compared to Q2 in cdf.
Similar performance for Vodafone across Qs

## Slide 13: POLQA AVG MOS (WhatsApp)
Similar performance for Vodafone in POLQA avg MOS for WhatsApp across Qs.
Three having small improvement in POLQA Avg MOS for WhatsApp service, mainly visible from p20 percentile

## Slide 14: POLQA <1.6
Small degradation observed in Vodafone from Q4 compared to Q2 in POLQA <1.6 rate in WhatsApp calls

## Slide 15: CST
Improvement in CST in Q4 for Vodafone compared to Q3 and Q2
Three showing degradation in CST in Q4 compared to Q2, mainly on higher percentiles.

## Slide 16: FDTT DL (7s)
Vodafone improved in Q4 compared to Q3 in FDTT DL throughput performance, having similar performance compared to Q2. Lower share of low-rate sessions observed in Q4 compared to Q3.
Three having similar performance in Q4 vs Q3, showing lower low-rate sessions in Q4 compared to Q3, mainly below 20 & below 5mbps.

## Slide 17: FDTT UL (7s)
Vodafone having similar performance in Q4 compared to Q3 in FDTT UL throughput performance. Lower share of low-rate sessions observed in Q4 compared to Q3.
Three having lower low-rate sessions in Q4 compared to Q3, mainly below 20 & below 3mbps.

## Slide 18: FDFS DL
Vodafone degraded FDFS DL throughput in Q4 compared to Q3, having similar performance as in Q2.
Three showing similar performance in Q4 and Q3.

## Slide 19: FDFS UL
Vodafone improved the FDFS UL throughput in Q4 compared to Q3, showing also better transfer time in UL.
Three having similar performance in FDFS UL throughput compared to Q3.

## Slide 20: Interactivity
Worse performance for Vodafone in Q4 in interactivity RTT compared to Q3.
Three having similar performance in interactivity RTT and packet error ratio compared to Q3

## Slide 21: Browsing
Similar performance for Vodafone and Three in Q4 compared to Q3 in browsing time to 1MB.

## Slide 22: Conclusions
Operator | Main Finding | Recommendation | Potential Scoring Impact
VFE | Higher data failure ratio in all data test, but specially in FDFS DL&UL in Q4 compared to Q3. | E2E analysis | Data services Success Ratio ('Most reliable’) (FDFS DL&UL, Browsing and Video)
 | Improvement in CST in Q4 compared to Q3 and Q2 |  | CALL SETUP TIME (‘Best Network’)
 | Improvement in FDTT DL throughput performance in Q4 vs Q3 (* due to change in the CORE), matching similar trends as in Q2 |  | FDTT DL Throughput
 | Degradation in FDFS DL throughput performance in Q4 vs Q3 (* due to change in the CORE), matching similar trends as in Q2 |  | FDFS DL Transfer Time
 | Higher Interactivity RTT in Q4 compared to Q3, similar figures as in Q2 (*). London showing poorer performance in Q4 compared to Q2. | E2E analysis | Interactivity RTT (‘Best Network’)
 | Throughput performance when connecting to 3UK MOCN nodes mimics the 3UK performance |  | FDTT and FDFS DL&UL Throughput
 | Better Throughput performance when connecting to VFUK MOCN nodes. This relates with the higher NR TDD utilization |  | FDTT and FDFS DL&UL Throughput
Three | High unqualified data sessions in FDFS DL HTTPS test (not RF related) still present in Q4 in NSA CDR. In SA CDR this problem is not present. | E2E analysis. E2E core tracing needed | FDFS DL Success Ratio ('Most reliable')
 | Lower Call Success ratio in Q4 in London compared to Q3 (higher number of VoLTE failures) | Detail Log analysis of failures cases | Call Success Ratio ('Most reliable')
 | Degradation observed in POLQA AVG MOS in Q4 compared to Q3 mainly in Belfast and Sheffield |  | POLQA Avg MOS
 | Throughput performance when connecting to VFUK MOCN nodes mimics the VFUK performance |  | FDTT and FDFS DL&UL Throughput
 | Better Throughput performance when connecting to 3UK MOCN nodes. This relates with the higher NR TDD utilization |  | FDTT and FDFS DL&UL Throughput
(*) In 2025 Q4 Vodafone core is CISCO CORE (as in 2025 Q2) and in 2025 Q3 it was COSMOS ERICSSON